Almitra,
This is an excellent idea. Send poster first, we can have a seperate poster
board for such innovative ideas.
Vishwas kale.
----- Original Message -----
From: Almitra Patel <almitrapatel@rediffmail.com>
To: <klean@vsnl.com>; <Water@bol.net.in>
Sent: Sunday, April 07, 2002 11:32 PM
Subject: Poster for IEA


Dear Mr Chilekar

On 9th April 2002, our CM Mr S M Krishna is going to inaugurate a stretch of
road made with Polymer Modified Bitumen using waste carry-bags.  Would IEA
be interested in my preparing a Poster detailing the technical advantages of
such roads which also solve waste-recycling problems for cities?  Can this
be put up without payment, like the Students' presentations?

Almitra

# Wonderful use for thin plastic road-waste

## Discarded thin-plastic carry-bags are a menace.

## In town they clog drains, cause flooding, choke animals that eat them and are unsightly.

## Strewn across fields, they  block germination and prevent rainwater absorption by soil.

## Recycling plastic by melting releases fumes,            and is only possible 3-4 times.

## Toxic contents might leach into recycled   water-pots or water-pipes.

# Shredded plastic is a great additive for tar roads.

## Burying plastic forever into roads is the safest.

## A new KK* Blower under patent in Bangalore  introduces it uniformly into Hot-Mix Plants.

## Polymer-Modified Bitumen is in use since long.

## It is approved in the Indian Roads Congress’ Special Publication 53 guidelines, 1999.

## Best results are with 8% waste by weight in 80/100 grade bitumen.

## * KK Plastic Waste Mgt, Yelachenhalli, Bangalore 560078, Fax 080-6657725

# Advantages of waste plastic in asphalt road surfaces

## Reduced penetration and ductility, a higher softening point, less rutting and cold cracking.

## Marshall stability value is initially 25% better, later 200-300% better than unmodified roads.

## Test samples show 260% improved resistance to water-soaking, hence ideal for sub-grade.

## 100% improvement in fatigue life of roads.

## Greatly reduced road cracking after 1 year on Bangalore-Mysore Rd, vs unmodified road.

# How Much Plastic?  How Many roads?

## Each 5-member family’s use of 5 gm plastic bags a week, all-India = 52,000 tons a year.

## Assume 50% of this is available for roads.

## 1.5 tons plastic goes into avg 1 km road.

## So resurfacing just 35,000 km of roads a year will absorb all this littered waste. This is just

## 3.5 % of India’s 1 million km surfaced roads.

## (1.1 million km more roads are unsurfaced).

# Waste Minimisation and Infrastructure Improvement

## India spends Rs 35,000 crores  a year on road construction and repair, including

## Rs 100,000 crores a year just on maintenance.

## Roads lasting 2-3 times longer, will save us         Rs 33,000 crores a year in repairs,            plus reduced vehicle wear and tear.

## 8% by weight of plastic waste in bitumen = a saving of 0.4% of bitumen by weight in roads.

## Negligible extra cost for far better infrastructure.

# Political Will is the Missing Factor

## Plastic bags disposal need never be a problem:

## A street price of Rs 5 per kg will reduce litter.

## Corruption in road works is a major obstacle:

## State and Central PWDs and National Highway Authority must incorporate waste-plastic modified bitumen into all road specifications.

## BOOT road-builders will benefit the most.

## For info, contact: kakbest@hotmail.com

## or    almitrapatel@rediffmail.com