30.6.2003

Dear Madam,

We were very pleased to meet you during your visit to Amravati recently.

During our site visits, you had advised us to incorporate more details about the project for our client Mr. Ashish Dhonde.

Attached herewith, kindly find the details of the said proposal. We are not in a position to provide detailed drawings of plant / equipment at this juncture.

In addition to this, our clients have surveyed and found sites that fit the criteria listed by you during your visit. The list of proposed sites matching these criteria has been submitted to the Commissioner, Amravati Municipal Corporation.

We have incorporated all details you required. However, if you require any additional details, kindly ask us and we will provide these promptly.

We look forward to your kind approval of the project.

Warm Regards,

Rajendra Chandrachud
Salus Technologies Pvt. Ltd.
Tel: +91-20-5430902

Rajendra Chandrachud salus@email.com

http://www.salustechnologies.com/

Project Report

for

Municipal Solid Waste Treatment project

Amravati Municipal Corporation

| Contractor: | Mr. Ashish Dhonde |
| --- | --- |
| Contact Person: | Rajendra Chandrachud |
| Designation: | Managing Director |
| Date: | 28 June 2003 |

This document is the property of Salus Technologies Pvt. Ltd. and its contents shall not be divulged to any third party without the express written consent of Salus Technologies Pvt. Ltd.

1.  Introduction:

This proposal was prepared for Shri Ashish Dhonde, Amravati

This document outlines in detail the proposal for solid waste management. and the methods in which the objectives above can be achieved.

Detailed calculations about the proposed compost plant are provided in accordance with the requirements of Smt. Almitra Patel, consultant for Amravati Municipal Corporation.

During the preliminary visit by Smt. Patel, several criteria were discussed for the best site locations for setting up the compost plant. Such sites have been identified by Shri Dhonde and submitted to the Amravati Municipal Corporation.

2.  Terms of Reference:

- The Client: Mr. Ashish Dhonde, Amravati

- The Consultant: Salus Technologies Pvt. Ltd., Karve Nagar, Pune 52.

- MT: Metric Ton

- TPD: Tonnes per day

- MGD : Municipal Garbage Depot

- Garbage : Domestic Solid waste collected from garbage bins within the city.

Project Proposal for Continuous Operation:

This section of the proposal describes:

- The methods of treating the garbage on a continuous basis

- The investments that will have to be made by the Client for constructing the project.

- The costs of operating the treatment process on a continuous basis.

- The expected returns on investment.

3.  Composting Process:

- Garbage is screened for large items such as auto tyres, glass bottles, plastic bags, tube lights, branches of trees, polystyrene, metal scrap and any other non degradable material that is immediately visible.

- Garbage is sprayed with composting bio-culture at the rate of 1 litre per tonne of garbage.

- The garbage is arranged in heaps for each day.

- Each heap is turned once every 7 days to allow even distribution of composting microorganisms within the garbage mass.

- The process is continued for a period of 45 days until the garbage turns black. This is now compost

- If the compost is too wet to handle, it will be spread out to dry.

- Once the compost is adequately dry, it will be screened for non degraded material such as plastic bags, glass, plastic etc. Screening and separation machinery will be used for this purpose.

- The compost will be then passed through a milling machine. Milling machine will be a shredder that will reduce the compost to a uniform size less than 5 – 10 mm in length and 1 – 2 mm in width.

- Compost will be disposed by loading directly into trucks and delivering to fields where required.

- Nutrients may be require to be added to enhance the quality of compost in certain cases and can be determined only after testing the compost.

- The screened residue (plastic etc.) will be sold to scrap merchants in the area as a source of revenue.

Below is a schematic representation of the process

4. Capital Investments:

|  | Description | Qty | Amount (Approx.) |
| --- | --- | --- | --- |
| 1. | Construction of asphalt surface and external works | 8000 sq. m. | 5000000.00 |
| 2. | Construction of storage space for bagged compost, bags and cultures. | 1000 sq.m. | 5000000.00 |
| 3. | Misc. Office buildings for staff & workers | 100 sq.m. | 1000000.00 |
| 4. | Water tanks (Sintex type) | 2000 litres | 16,000.00 |
| 5. | Pumping + Plumbing Equipment | - | 125000.00 |
| 6. | Electrical Installations incl. power connection | - | 200000.00 |
| 7. | Bore Well | 1 | 25000.00 |
| 8. | Platforms etc. | 1 | 25000.00 |
| 9. | Fencing (provisional amount; optional) | - | 500000.00 |
| 10. | Leachate Tank | 50 cu.m. | 600000.00 |
| 11. | Screening Machinery |  | 500000.00 |
| 12. | Milling Machinery | - | 1500000.00 |
| Total: | 14,491,000.00 |
| Rupees One Crore Forty Four Lakhs Ninety One Thousand Only. |  |

Important notes on costing for capital infrastructure:

- The asphalt surface is required below garbage to trap leachates generated by garbage. Leachates should not be allowed to percolate the ground and will be diverted to leachate tank (item 11) and treated further before disposal.

- Leachates allowed to percolate into the ground may ultimately reach water table and cause contamination.

- Leachate reduction will be achieved by spraying leachates back on to the composting heaps of dry garbage.

5. Calculations for Operating Cost:

5.1 Assumptions:

- Garbage produced per day is 75 tons.

- Adequate water is available.

- Operating Cost is calculated for monthly operations.

Based on data from Central Pollution Control Board, India, total Biodegradable waste from the project will be about 44% of the total mass. Thus from 75 TPD garbage, we can get 33 tonnes per day compostable material.

In addition, from TERI Report No. 97/ED/52 (1998), the total recyclable waste is estimated at 15 – 17%. Thus total recyclable material obtained will be 11 tons per day.

# 5.2 Mass Calculations Summary (Daily)

| Sr | Description | Weight (tons) | Balance |
| --- | --- | --- | --- |
| 1 | Total Mass Incoming | 75 | - |
| 2. | Pre Screen for tyres, battries etc | 0.25 | 74.75 |
| 3. | Culture Spraying | 7.25 (Add) | 82 |
| 4. | Total Compostable | 33 | 49 |
| 5. | Total Recyclable | 11 | 38 |
| 6. | Non Recyclable | 1 | 37 |
| 7. | Leachates (from degradable only) | 0.5 | 36.5 |
| 8. | Non degradables to Land Fill | 8 | 28.5 |
| 9. | Evaporation | 10.5 | 18 |
| 10. | Compost Obtained | 18 | 0 |

5.3 Energy Consumption Calculations (Daily):

| Sr. | Description | Consumption (kW) |
| --- | --- | --- |
| 1. | Borewell Pump | 5 |
| 2. | Leachate Tank Pump | 1 |
| 3. | Segregator and Miller | 100 |
| 4. | External Lighting | 1 |
| 5. | Office Lighting | 1 |
|  | Total: | 108 |

5.4 Water Consumption Summary (Daily)

| Sr. | Description | Consumption (litres) |
| --- | --- | --- |
| 1. | Composting Cultures | 7500 |
| 2. | Machinery Washing | 1500 |
| 3. | Washing and Cleaning (labourers) | 2000 |
| 4. | Toilets etc | 500 |
| 5. | Drinking | 200 |
| 6. | Other Maintenance | 50 |
| 7. | Gardening (recycle from 3) |  |
|  | Total: | 11750 |

5.5 Operating Costs:

|  | DESCRIPTION | AMOUNT (Rs.) |
| --- | --- | --- |
| 1. | Composting Cultures | 54450 |
| 2. | JCB operations | 25000 |
| 3. | Staff + Labour (salaries) | 50000 |
| 4. | Directors’ Salaries (10 directors) | 50000 |
| 5. | Diesel and Fuels | 10000 |
| 6. | Communication | 10000 |
| 7. | Water | 15000 |
| 8. | Manual Screening (75 TPD) + Post compost screening | 50000 |
| 9. | Electricity for pumps and operatives office rooms | 21000 |
| 10 | Disposal of non-recyclable material | 25000 |
| 11. | Routine Testing of Compost for nutrients etc. | 5,000 |
| 12. | Maintenance of Plant and Machinery | 25000 |
| 13. | Miscellaneous Expenses | 10000 |
|  | Total Operating Costs /month | 350450.00 |

#### 6 Profitability of Operations

The Compost Plant will generate about 18 tons of compost per day.

Assume a selling price of Rs. 1500 per ton and transport by buyer.

Thus, daily revenue for 18 tons compost = 18 x 1500.00 = 27,000.00

Additionally, we will get about 11 tons of recyclable material from this waste.

Assuming a selling price of Rs. 750.00 per ton, we will generate an additional revenue of

= 750 x 11

= Rs. 8250

Thus, gross daily revenue = 27,000 + 8,250

= Rs 35250 .00

#### Gross Monthly revenue = 35250.00 x 30

= Rs. 1057500.00

# Annual Revenue: 10,57,500 x 12 = Rs. 12690000.00

Thus the project will provide an annual gross return of Rs 1,26,90,000.00

6.1 Total Operating Costs per year

| Sr. | Description | Cost |
| --- | --- | --- |
| 1. | Operating Cost (From table above) 350450 x 12 | 4205400.00 |
| 2. | Marketing Expenses | 500000.00 |
| 3. | Insurance | 25000.00 |
| 4. | Auditing and Other Company Expenses | 25000.00 |
| 5. | Statutory Taxes (Approximate) | 200000.00 |
| 6. | Royalty to Corporation on Compost sold/produced on 75 tons @ Rs. 50 per ton (75 x 50 x 365) | 1368750.00 |
|  | TOTAL: | 6324150.00 |

| Net Annual Income | = Gross Revenue – Total Operating Cost = 12690000.00 – 6324150.00 = 6365850.00 |
| --- | --- |

7.0 Landfill criteria and related issues:

During the visit to the corporation’s existing garbage depot, several heaps of construction rubble comprising demolished concrete, brickbat and mud were seen.

The Amravati Municipal Corporation should identify landfill sites in the area and dump all earthen material, construction rubble and other similar items at this location. This would eliminate double handling of this material, which, on all accounts will be free from organic waste.

The Corporation is also requested to ensure that toxic waste from industries does not enter the treatment plant and separate provisions be made for disposal of the same.

In addition, the Corporation should identify landfill sites where the contracor can dispose all non-hazardous, non-recycle waste. This waste would be that left after screening from final compost. This, any material adhering to this coponent  of waste will have fully composted, thereby eliminating risk of contamination.