## Slide 1: HOTEL WASTE MANAGEMENT OPTIONS
WAKE UP CLEAN UP
BANGALORE

## Slide 2: MANAGE FOOD WASTES ONSITE
Keep food wastes unmixed with other wastes like plastics and disposable catering items.
Minimise plastics in catering items:
NO plastic tablecloths
NO thermocole plates or glasses
Use washable catering supplies

## Slide 3: BIOGAS IS THE BEST OPTION
With LPG prices rising, it is best to produce cooking gas from your food wastes, even if it meets only a part of your cooking gas needs.
Compact terrace or backyard units are best and on display in these stalls.
Design for the highest average quantity expected . DO NOT OVERLOAD THE UNIT !

## Slide 4: COMPOSTING IS YOUR NEXT OPTION
Many options are available and live models are on display to the right of the Jail Cells bldg :
A thippe or compost pit if you have space
A trench along a boundary wall
Two biobins on the terrace for upto 40 kg waste
Above-normal festival day waste in excess of biogas capacity can go for composting

## Slide 5: EXPLORE ANIMAL FEED OPTIONS
Keep separate dustbins for pre-cooking waste and for cooked waste from food plates
If there is a cow-keeper or goshala near you, send your uncooked waste to them as fresh as possible preferably twice a day. Ask them if there is anything special to avoid, like muddy roots or green chillies.

## Slide 6: FOOD LEFTOVERS FROM PLATES
This is perfect for piggeries. Do not wash it into sink. Contact Mr Ramakanth 93412 50158 vedarama_kanth@yahoo.com
Keep coffee grounds and tea leaves out of this piggery waste. Both are ideal for roses and other plants.

## Slide 7: SERVING-DISH FOOD SHARING
Partner with a homeless shelter or orphanage to
Share your leftovers from serving dishes, as
SKCV does in Vijayawada.
Three clean 5-litre stainless cans are filled after
lunch with all mixed veg, all mixed rice, all mixed
liquids. These are picked up at 3pm for serving
street kids @ Re 1 per plate.
Three clean vessels left for dinner leftovers are
kept in hotel fridge for early-morning pickup to
serve at breakfast.

## Slide 8: FOOD B ANK BY HOTELS
In Delhi, 12 five-star hotels supply leftover bread rolls, fruits etc and food to old age homes.
Refrigerated vans deliver leftover food also.
Lions, Rotary and various social organisations can help create these networks.

## Slide 9: MINIMISE PACKAGING WASTE
Require suppliers to provide supplies in reusable take-back packaging :
Soft -drink suppliers to take back their empties
Rice, dal etc supplied in cloth sacks instead of plastic.
Ecotels also minimise waste by keeping plants instead of flowers in hotel rooms and tables.