## Slide 1: IDEAL WASTE MANAGEMENT IN KOLAR SINCE 2014
Almitra H Patel
Member, Supreme Court Committee
for Solid Waste Management
in Class 1 Cities
almitrapatel@rediffmail.com
www.almitrapatel.com
1

## Slide 2: KOLAR CMC www.kolarcity.gov.in Pop 1.5 lac has NO SITE FOR WASTE MGT

## Slide 3: In May 2014 they planned for ‘zero waste’ to landfill
They called in Clean Clities Foundation for help.
(See www.cleancitieschampionship.org)
All streets and lanes were mapped using city
maps and GIS and the entire area sub-divided
into Micro-Pockets of 350-400 households.
Maistrys became Route Managers and planned
doorstep routes and timings for their 2-person
teams who are left strictly undisturbed.

## Slide 4: Door-to-door collection is in pushcarts with 4+4 covered 60-litre bins & 20 litre sorting basin

## Slide 5: A sorting-basin first receives waste, for dry waste to go into bags and wet into bins

## Slide 6: Two-person PK teams improvise, but keep wet and dry waste separate

## Slide 7: A double-handle helps to hang jumbo bags for paper and saleable plastic

## Slide 8: PKs can keep entire sale proceeds of all they collect, so doorstep sorting is good and absenteeism is low

## Slide 9: PKs take Copra-shells home for burning as fuel for hot water

## Slide 10: Homes giving wet-dry unmixed each day for a month can enter a prize lottery

## Slide 11: Each team covers 400 houses 6:30-10 am in 2 rounds. After 1st trip 4 bins and some bags are left briefly on road for pick-up

## Slide 12: Tractors promptly pick up bins 10am-12 in 2 trips, + 3rd trip for dry waste if reqd

## Slide 13: Every bin weighed on spring-scale before loading, to compile day’s pick-up data

## Slide 14: Wet waste is managed by ‘Stack’ Composting within five inner-city locations
Tractors back up to stacks and its bins are emptied directly in thin layers per stack.
So no manual handling of waste is needed.

## Slide 15: JULY ’14 KOLAR ADOPTED STACK COMPOSTING IN 5 SMALL SITES. This is 100 kg/day Wet waste x 1 month

## Slide 16: STACKS are formed on wood frames placed on stone supports

## Slide 17: This keeps waste off the ground to allow cold air into heap as hot air rises

## Slide 18: Stack composting is self-aerating. Needs no eqpt, power or labour, only 1-3 months’ time to stabilise waste.

## Slide 19: Waste is unloaded directly from tractors, in 8”layers , using more than 1 stack per day if needed

## Slide 20: Stacks can be close together as no turning is needed

## Slide 21: ONLY BIODEGRADABLE ‘WET’ WASTE is stacked, so unmixed collection is a must

## Slide 22: Stacks are ready for auction to farmers as early as 1 month of maturing

## Slide 23: Wood frames are re-used after farmers remove compost

## Slide 24: Even city-centre stacks are nuisance-free, but a visual barrier fence would help

## Slide 25: This is a demo of 100 kg/day in ward No 1, wet and dry waste separate

## Slide 26: This demo is 100 kg/day Dry Waste from same Ward No 1, on NH75

## Slide 27: Same PK team does afternoon sweeping. Little waste ends on roads if their doorstep collection covers every house

## Slide 28: All slum lanes are spotless

## Slide 29: Even unpaved lanes and drains stay clean with doorstep collection

## Slide 30: A complete ban on all-thickness plastic bags has helped immensely

## Slide 31: Now only management of construction waste obstructs the roads

## Slide 32: A ring of stones or sand-bags keeps sand off road and saves wastage

## Slide 33: Unrecyclable plastics like ‘kurkure’ sachets and thermocole can be shredded and used for ‘plastic roads’

## Slide 34: Storm-water drains have been cleared and fenced to keep out waste dumping

## Slide 35: So a Zero-Waste City can be a reality !
What is needed is unity of DC, Commissioner and Councillors and continuity of policy from year to year despite transfers or elections.