## Slide 1: Mixed waste dumping in Belhalli quarry pits, Bangalore
Almitra H Patel
Member, Supreme Court Committee for Solid Waste Management in Class 1 Cities
11 May 2016
almitrapatel@rediffmail.com
www.almitrapatel.com

## Slide 2: Bangalore’s Belhalli quarry is approached by a newly metalled road

## Slide 3: so that compactors can unload mixed waste into an unlined quarry, permanently polluting groundwater for decades !

## Slide 4: With mixed waste dumped on an unlined floor, the quarry is being partly lined

## Slide 5: The quarry is being partly lined with porous white fabric

## Slide 6: Covered with overlapping black plastic without waterproof welded seams

## Slide 7: The plastic rolls are draped over the edge of the quarrypit

## Slide 8: In token fashion without proper overlap.

## Slide 9: Mixed waste spread on the unlined quarry floor is covered with soil which serves no purpose.

## Slide 10: Using coarse organics as cover would help compost the dumped waste and make later biomining easier.

## Slide 11: Plastic is also draped in deep pockets on the quarry floor.

## Slide 12: The weak plastic is easily punctured in many places, with some big holes

## Slide 13: Shot-creting over weldmesh is being done along the bottom wall of the quarry

## Slide 14: Continuously for a few feet

## Slide 15: Without first removing fractured rock

## Slide 16: The loose upper rock is most dangerous

## Slide 17: As fractured giant boulders

## Slide 18: can fall any time

## Slide 19: Rocks falling onto the quarry floor.

## Slide 20: There are many dangerous overhangs

## Slide 21: And faces of loose fractured rock

## Slide 22: Fallen rock will create problems for effective waterproof lining of the quarry

## Slide 23: Loose rocks lying inside need removal

## Slide 24: Rocks on the surface also need removal

## Slide 25: To improve access to the quarry

## Slide 26: To widen the approach road

## Slide 27: And create more open space

## Slide 28: where mixed waste can be stabilised in windrows before filling into the quarry.

## Slide 29: The existing crusher should be given temporary permission to operate for another 6-12 months to clear all this.

## Slide 30: There is an existing pool 60ft deep (measured) unused by locals

## Slide 31: which is tempting for summer swimmers who drown here.

## Slide 32: This pit is clearly waterproof and needs no lining upto the waterline.

## Slide 33: The deep pool if needed can be drained into this porous pit with no pollution.